Lux IoT System
IoT Platform
External light contribution
Internal light balance
Light sensor

---
Lux IoT System - Diagram

---
External light contribution
LED controlled using PWM
PIC16F886
Nextion TFT
Serial Touch Display

---
Test Environment - Lux IoT System
Isolated Box
External light
Contribution LED
Light sensor
MAX44009
Internal light
Balance LED
ESP-32
PIC16F886

---
Luminance limits and PWM values selected
ESP32 / [NPN as switch : PWM Freq 1KHz , Resolution 16 bits -> factor 655 = 1%]
PWM Duty cycle %	Lux
37	146,88
43	171,36
51	195,84
57	220,32
63	244,8
69	269,28
75	293,76
81	318,24
87	342,72
Regular increment of 24.84 [lux] value.
Table 1: Result of empirical measures.

---
PIC16f886 / [NPN as switch: PWM Freq 1KHz , Resolution 8 bits -> factor 51 = 10%]
PWM Duty cycle %	Lux
0	0
10	39,78
20	79,56
30	122,4
40	159,12
50	195,84
60	244,8
70	269,28
80	318,24
90	367,2
100	391,68
Irregular increments of [lux] values.
Table 2: Result of empirical measures.

---
Duty cycle array construction
Duty Cycle Array
Array position	Value
0	37 x factor
1	43 x factor
2	52 x factor
3	57 x factor
4	63 x factor
5	69 x factor
6	75 x factor
7	81 x factor
8	87 x factor
Table 3: Duty cycle array, position and values.

---
	PIC16f886	ESP32
Minimum Lux Val	0	146,88
Maximum Lux Val	391,68	342,72
Table 4: Result of empirical measures.
Luxiot system
lux_low_limit	400
lux_high_limit	500
The limits were selected arbitrarily to provoke controlled failures.
Table 5: Luminance limits.